## Slide 1
Topic
DEPARTMENT OF CSE
COURSE NAME
COULD and devops
COURSE CODE
22CS2243F
subnetting

## Slide 2: What is subnetting ?
the process of dividing a large IP address block into smaller, more manageable sub-networks (subnets). This helps in improving network performance and security by segmenting traffic.
Key Terms-
**IP Address:** A unique address assigned to each device on a network.-
**Subnet Mask:** A 32-bit number that masks an IP address and divides the IP address into network and host portions.
2

## Slide 3
**CIDR Notation:** Classless Inter-Domain Routing notation, which is a compact representation of an IP address and its associated network mask (e.g., 192.168.1.0/24).

## Slide 4: Example Problem on Subnetting
Problem:
You have been assigned the IP address block 192.168.10.0/24. You need to create subnets that can accommodate at least 30 hosts each. How many subnets can you create, and what are the subnet ranges?
Solution:
1. Determine the number of host bits required:** - The formula for calculating the number of hosts is \(2^h - 2\), where \(h\) is the number of host bits. - To accommodate at least 30 hosts, \(2^h - 2 \geq 30\). - Solving for \(h\), \(2^h \geq 32 \Rightarrow h = 5\) (since \(2^5 = 32\)).

## Slide 5
2. Calculate the new subnet mask:- A /24 network has 32 - 24 = 8 host bits. –
We need 5 host bits for the hosts, leaving 3 bits for subnetting (8 - 5 = 3). - The new subnet mask will be /27 (24 + 3 = 27).
3. Determine the number of subnets:- The number of subnets you can create
is \(2^3 = 8\).

## Slide 6
4. Calculate the subnet ranges: - Subnet increment is \(2^5 = 32\) (since 5 bits are used for the host portion). - Subnet ranges: - Subnet 1: 192.168.10.0/27 (192.168.10.0 - 192.168.10.31) - Subnet 2: 192.168.10.32/27 (192.168.10.32 - 192.168.10.63) - Subnet 3: 192.168.10.64/27 (192.168.10.64 - 192.168.10.95) - Subnet 4: 192.168.10.96/27 (192.168.10.96 - 192.168.10.127) - Subnet 5: 192.168.10.128/27 (192.168.10.128 - 192.168.10.159) - Subnet 6: 192.168.10.160/27 (192.168.10.160 - 192.168.10.191) - Subnet 7: 192.168.10.192/27 (192.168.10.192 - 192.168.10.223) - Subnet 8: 192.168.10.224/27 (192.168.10.224 - 192.168.10.255)

## Slide 7: conclusion
In this example, you can create 8 subnets from the 192.168.10.0/24 network, with each subnet supporting up to 30 hosts. The new subnet mask is /27, providing an increment of 32 addresses per subnet. This practice helps in organizing and managing IP addresses efficiently, ensuring that network traffic is well-segmented and easier to manage.

## Slide 8
THANK YOU
Team – CLOUD and devops